車輛動態與控制

核心能力一  轉移函數之控制系統

- 何謂轉移函數?

- 何謂頻率響應?

Δ frequency Response：系統輸入為 正弦波      討論的Frequency輸出

Consider a linear time–invariant stable system G(S).

If the input is , then the steady- state output is  where

,

Thus

複數表示法         相量表示法

- 何謂波德圖?

Δ Bode Plot  波德圖

As different from polar plot, Bode plots are sketched in two parts, namely the magnitude part and the phase part.

- Magnitude of  is drawn versus the frequency

For convenience, the magnitude is plotted based on the logarithmic operator

(取log是為了方便相加)

∵

if we take logarithmic operation , then

which can be obtained by adding all the individual  together

- Phase of ,

If

By adding all together,  is then obtained.

- 比例、微分、積分控制器之形式及特性為何?

控制器分類

R      E                       Y

+

-

- 比例控制(proportional control)

特性：

- 改善穩定度

- 改善穩態誤差

- 降低靈敏度

- 抑制雜訊

- 微分控制 (derivative control)

特性：

- 改善穩定度

- 提升響應速度

- 增加雜寬

- 放大雜訊 (x)

- 積分控制 (integral control)

特性：

- 增加系統type消除穩態誤差

- 降低響應速度 (x)

- 易造成系統不穩定 (x)

- 比例+微分

- 比例+積分

- 比例+積分+微分

例題 1:

When the system shown in the Figure 1-(a) is subject to a unit step input the

system output responds as shown in Figure 1－(b) Determine the values of T and K from the response curve.

Figure 1-(a)

例題 2:

Estimate the transfer for the” Bode plot” for the magnitude shown in the figure. Assume it is minimum phase.

∴ K=3000

∵dB

∴

例題 3:

A mechanical system is shown in Figure. The motion of mass M is small and is constrained by a spring with constant k and a damper with coefficient c. A rigid bar is used to connect the mass and the disk. The motion of the disk is constrained by a torsional spring with spring constant G. The inertia of the disk is J and the friction of the disk is negligible. Derive the transfer function of this system in which y is the output and f(t) is the input.

Sol:

The free body diagrams are shown below

The dynamic equation

..... (1)

.............. (2)

Because of

(2) into (1)

Taking Laplace transforms and we can get the transfer function of the system

例題 4:

例：Consider a system shown in Figure. Suppose  Find the steady- state response y(t)

重疊定理響應

Sol：

(1)

虛         實

∴

(2)

∴

( the total response

核心能力二 狀態空間之控制系統

  - 系統之可控制性

狀態空間設計(State space design)

古典控制

U(s)              Y(s)

近代控制

U(s)                Y(s)

X:狀態變數

例題:	y(t)

k

β

轉移函數法：

狀態空間法：

狀態空間之控制器設計(Controller Design in State Space)

可控制性(Controllability)

條件：

控制性矩陣

若

  - 何謂狀態回授控制?

控制器設計

- 先決定控制閉迴路系統之理想極點或理想特徵值

例題1: 一控制系統其狀態方程式如下:

如果控制器設計為

其中a、b 為常數。當此閉迴路控制系統為穩定時，求出a、b之範圍並以a為橫軸，b為縱軸，畫出a-b之關係圖。

例題2:

- 定義狀態變數  以及輸出 y , 列出狀態方程式。

- 設計狀態回授控制器  使得閉迴路特徵值為

- 將此系統以下列方塊圖表示

+-               +-

Sol:

(1)

(2)

代入

(3)

+	+

-	-

例題3:

Give a system , if the state space representation of the system is     求,b,g?

Sol:

例題4:

例:

V為輸入電壓，VC為輸出電壓

求狀態方程式及轉移函數

Sol：

電路方程式為

轉移函數法(兩邊取拉式轉換)

狀態空間法

令

# Text boxes

轉移函數

G(s)

輸出

輸入

M

y(t)

無摩擦

m=1

y

r

u

2S

r

y

2